## Slide 1: Introduction to ESIPAP Computing Sessions
Wednesday 10 – Thursday 11 February 2021
ERIC CHABERT - ERIC CONTE

## Slide 2: Goals of the computing sessions
Computing is required for instrumentation purposes:
  Simulation of sensor
  Data acquisition
  Data analysis
  Algorithm and reconstruction of physics objects
Computing sessions target to apply your theoretical knowledge:
  Instrumentation
  Software programming in C++
  Using specific tools of high energy physics: ROOT
Working by yourself and experimenting
Getting the good practice

## Slide 3: Physics Context

## Slide 4: The CMS (Compact Muon solenoid) detector

## Slide 5: The CMS (Compact Muon solenoid) detector

## Slide 6: Silicon strip tracker

## Slide 7: Silicon strip tracker
CMS silicon strip tracker in few numbers:
15 000 modules
Surface: ~ 200 m2
106 channels
Instrumental activities
R&D
Construction
Operation (online)
Alignment & calibration
Offline analyses
Simulation
Radiation damages evaluation
…
Performances:
Hit resolution: 20-40 μm
Hit efficiency > 98% (at high Pile-Up)
Timing alignment accuracy: 1ns
…

## Slide 8: Silicon strip tracker
During its operation it is important to monitor environment conditions:
  Temperature
    Leakage current
    Noise
    Thermal dissipation
    Radiation damages
    …
  Humidity
    Dew points & condensation
    Front End electronics
    …
Monitoring tools
Several probes are used to monitor that:
  On-board sensors
  External sensors
Some are Arduino-based!

## Slide 9: Computing session aims
Slow control
  Using a dedicated electronic board (Sense Hat) read by a Raspberry
    Monitor the temperature & humidity
    Send warning when conditions are not fulfilled
Offline analyses
  Calibration of the temperature sensors
  Evaluation of the sensor resolution
3. Simulation
  Basic simulation with the Geant4 package of a CMS silicon strip sensor
Instrumental activities
R&D
Construction
Operation (online)
Alignment & calibration
Offline analyses
Simulation
Radiation damages evaluation
…

## Slide 10: DATA USED IN THE COMPUTING SESSIONS

## Slide 11: Sensors to study
CONDITIONNING
Analogic Front-End + ADC + Signal treatment
2 channels
= collected charged
= energy (0 to 255)
Temperature
Relative humidity
Pressure

## Slide 12: Summary on ADC sensitivity
 | Pressure | Temperature | Humidity
Full scale | 13.25 hPa to 2013.25 hPa | -20°C to +100°C | 0% to 100%
ADC resolution | 12 bits | 12 bits | 8 bits
Sensitivity | 0,49 hPa | 0,029 °C | 0,39 %

## Slide 13: Organization

## Slide 14: Organization in sessions
Session 1
Wednesday
Thursday
Introduction
Reading binary data
Developing a C++ class
Combining classes
Analyzing data with ROOT
Session 2
Session 3
Session 4
9:00
12:15
14:00
17:15

## Slide 15: Multi-plaTform development
Windows
Linux
Mac OS X
Raspberry board (ARM architecture)

## Slide 16: Tools to USE
Saving and preserving code on the internet: site github
Sharing codes with others.
Generating automatically documentation of your code (in HTML and LaTex)
Building a C++ project witch several files
(Linux / MacOSX only)

## Slide 17: Skill assessment
Individual work is required
Evaluation over 8 categories
For validating the module
  Minimum level must be reached for all the 8 categories
  Satisfying level for at least 4 categories